## Slide 1: Aircraft Turnaround
Adnan Mahmood
Notes: http://www.safranmbd.com/activites/electric-green-taxiing-system/

## Slide 2: What happens during turnaround?
Ground Handling
Cabin services
  Cleaning passenger cabin
  Replenishment of on-board consumables
Catering
  Unloading of unused food/drink
  Loading of fresh food and drink

## Slide 3: What happens during turnaround?
Ramp services
  Guiding aircraft in/out of parking
  Refueling, passenger stairs, luggage/cargo handling
  Etc, etc.
Passenger Service
  Check in, gate arrival, passenger lounge
Notes: http://www.safranmbd.com/activites/electric-green-taxiing-system/

## Slide 4: What happens during turnaround?
Field operations service
  Dispatched aircraft
  Maintains communication with rest of airline and ATC
Taxiing
  Movement of an aircraft on the ground, under its own power

## Slide 5: Where can we improve?
Difficult if it involves passengers
  Unpredictable
  Safety checks
Cabin services
  You can only improve cleaning and restocking so much

## Slide 6: Where can we improve?
Getting loads on/off aircraft
  Possible redesign of luggage hold?
  Bags are different shapes and sizes
  Can also tie in to aerodynamics if we are designing a new fuselage

## Slide 7: Where can we improve?
Taxiing
  A320 spends, on average, 3.5 hours a day taxiing
  Uses 570L of fuel
  Can increase with longer waiting times
  Possible use of electric taxiing to reduce the fuel burnt

## Slide 8: Taxiing?
Electric taxiing currently in development
Easyjet testing Electric Green Taxiing System (EGTS)
Being developed by Honeywell and Safran

## Slide 9: EGTS
Using the airplane’s Auxiliary Power Unit (APU) generator to power motors in the main wheels, the Electric Green Taxiing System allows aircraft to taxi without requiring the use of primary engines. Each of the aircraft’s powered wheels is equipped with an electric motor-reduction gearbox-clutch assembly to drive the wheels, while unique power electronics and system controllers give pilots total control of the aircraft’s speed, direction and braking while on the ground.
Time for a video!!!

## Slide 10: EGTS
Lower fuel burn
  Save up to 4% in total fuel consumption
Increased Performance
  Aircraft able to pushback and go more quickly
  Reduces gate and tarmac congestion
Greener operation
  Reduced emissions
  Lower carbon emission taxes

## Slide 11: EGTS
Added value
  No need for tugging and any associated equipment
  Less use of main engines extends engine life
  Enhances ground crew safety
  Reduces airport noise

## Slide 12: EGTS
Is it all too good to be true?
  Does added weight on the wheels cancel out any savings made?
  What happens if it breaks down? Can the plane still be moved by other means?
  Heavy use of electronics? How much do we know about this?
  Brings about issue of time?
  Is it original?

## Slide 13: Other possibilities?
Very little research into reducing turnaround time
Mechanical breakdown can make the whole issue pointless
Reducing turnaround time would involve making the processes more efficient
How innovative and exciting is this compared to the rest as a Round 1 proposal?